## Slide 1
UNIVERSITY OF LEICESTER · GROUP 1
Urban Change Detection
Using CNN Models
Application of CNN Models to Remote Sensing Using Satellite Imagery
Dataset: LEVIR-CD | Models: U-Net & Siamese U-Net | Assignment 2 — Group Research Project
U-Net IoU 0.614 F1 0.726 Competitive with published FC-EF baseline

## Slide 2
Presentation outline
2 / 12
01
Problem Statement & Motivation
02
Dataset — LEVIR-CD
03
Model Architectures
04
Training Configuration
05
Results & Analysis
06
Discussion & Limitations
07
Conclusions & Future Work

## Slide 3
Problem statement & motivation
3 / 12
68%
of world population projected to
live in urban areas by 2050 (UN)
Rapid urbanisation drives land-use change globally
Manual inspection of satellite imagery is impractical at scale
Conventional image-processing fails on high-dimensional data
CNNs can learn spatial representations without manual feature engineering
Objective: Detect per-pixel urban change (building construction/demolition) between two co-registered satellite images captured at different times.

## Slide 4
Dataset — LEVIR-CD
4 / 12
7,120
Training pairs
1,024
Validation pairs
2,048
Test pairs
Resolution:
0.5 m/pixel — fine enough to detect individual buildings
Image size:
256 × 256 px patches (cropped from 1024 × 1024 originals)
Coverage:
20 cities in Texas, USA — collected 2002–2018
Class balance:
Changed pixels ≈ 3–5% of total — significant imbalance
Labels:
Binary masks: 1 = changed (new build / demolition), 0 = unchanged
Source:
Google Earth very-high-resolution imagery

## Slide 5
Model 1 — U-Net (early fusion baseline)
5 / 12
6-ch Input
A + B
Encoder
4 stages
Bottleneck
512 ch
Decoder
4 stages
Output
1×H×W
← skip connections →
Input:
6-channel tensor: pre-change (RGB) + post-change (RGB) concatenated
Encoder:
4× DoubleConv + MaxPool → 32 → 64 → 128 → 256 channels
Bottleneck:
DoubleConv block at 512 channels, 16×16 spatial resolution
Decoder:
4× ConvTranspose2d + skip concatenation + DoubleConv
Output:
1×1 convolution → single logit map → sigmoid → change probability
Parameters:
~7.76M | base_channels = 32

## Slide 6
Model 2 — Siamese U-Net (shared encoder)
6 / 12
Image A (pre-change)
Shared Encoder
Image B (post-change)
Shared Encoder
|f_A − f_B|
Absolute feature
difference at each
encoder scale
Decoder
4 stages
Change
Mask
Key advantage: Comparison happens in learned feature space, not raw pixels — more robust to illumination and atmospheric differences between time steps.
~11.64M parameters | Encoder shared (applied twice per forward pass)

## Slide 7
Training configuration
7 / 12
Hyperparameter
Value
Rationale
Optimiser
AdamW
Decoupled weight decay — better generalisation than Adam
Learning rate
3 × 10⁻⁴ (initial)
Reduced by ×0.5 when val IoU plateaus (patience = 3)
Scheduler
ReduceLROnPlateau (max, ×0.5)
Adaptive — fine-grained convergence after initial learning
Loss
Dice-BCE (α = 0.5)
BCE stability + Dice robustness to class imbalance
Threshold
0.45
Slightly below 0.5 to boost recall on minority change class
Batch size
8 | Epochs: 50
Checkpoint saved at every new best validation IoU
Augmentation
Horizontal + vertical flip (p=0.5)
Applied to A, B, and mask consistently
Both models trained under identical conditions for a fair architectural comparison.

## Slide 8
Test set results — LEVIR-CD
8 / 12
U-Net (early fusion)
Siamese U-Net
0.6138
IoU (primary)
0.7261
F1-Score
0.9809
Accuracy
0.7991 / 0.7374
Precision / Recall
0.5000
IoU (primary)
0.6576
F1-Score
0.9757
Accuracy
0.7217 / 0.6133
Precision / Recall
Better on all 5 metrics

## Slide 9
Training dynamics — IoU progression
9 / 12
Chart: Epoch
| 1 | 5 | 10 | 15 | 20 | 25 | 30 | 36 | 40 | 45 | 50
U-Net | 0.258 | 0.48 | 0.54 | 0.565 | 0.582 | 0.591 | 0.625 | 0.632 | 0.62 | 0.615 | 0.608
Siamese U-Net | 0.135 | 0.4 | 0.506 | 0.505 | 0.505 | 0.506 | 0.498 | 0.492 | 0.5 | 0.497 | 0.495
U-Net: Steady improvement to epoch 36 (best IoU = 0.632), then gradual LR decay
Siamese: Rapid early gains, plateau from epoch 23 — harder optimisation objective

## Slide 10
Comparison with published baselines — LEVIR-CD
10 / 12
Chart: 
| FC-EF (Daudt 2018) | FC-Siam-Diff (Daudt 2018) | This project — U-Net | This project — Siamese | BIT (Chen 2021) | ChangeFormer (Bandara 2022) | SNUNet (Fang 2021)
IoU | 0.617 | 0.647 | 0.614 | 0.5 | 0.717 | 0.706 | 0.733
F1-Score | 0.755 | 0.783 | 0.726 | 0.658 | 0.833 | 0.823 | 0.845
Our U-Net (IoU 0.614) is competitive with the published FC-EF baseline (0.617), validating a correct and well-calibrated implementation.

## Slide 11
Discussion & limitations
11 / 12
Why U-Net outperformed Siamese U-Net
Harder optimisation
Shared-encoder constraint forces one feature space for both time steps — tougher without pre-trained weights
Feature alignment
Absolute difference loses direction of change; more sophisticated fusion strategies may help
Training budget
Siamese architectures generally need more data/epochs to reach full potential
Key limitations
No pre-trained encoders
Limited augmentation
Fixed binarisation threshold
CPU training only
No test-time augmentation

## Slide 12
Conclusions & future work
U-Net:
IoU 0.614, F1 0.726 — competitive with published FC-EF baseline (0.617)
Siamese:
IoU 0.500, F1 0.658 — plateau from epoch 23, harder optimisation from scratch
Insight:
Simple early-fusion CNN trained carefully beats more complex architectures without pre-training
Metrics:
Accuracy (~98%) is misleading — IoU & F1 are the meaningful metrics for imbalanced change detection
Future work
Pre-trained ResNet / EfficientNet encoder (+5–10 IoU points expected)
Attention mechanisms (SE blocks, CBAM) in the decoder
Larger 512×512 patches + GPU training + test-time augmentation
Transformer-based architectures: BIT, ChangeFormer (published IoU ~0.71–0.73)